## Slide 1
Location: Dzaleka
Lat: -13.671088
Long: 33.876118
Alt: 1420 masl
Nominal depth: 70m
SWL: 10mbgl
Steel Surface Casing: 3m
Surface Casing grouted
6’’ PVC casing cement sealed to 5 mbgl
6’’ PVC blank casing
6’’ PVC slotted casing: 1mm slots
Backfill above bentonite seal
Bentonite seal above gravel pack
Borehole annulus gravel packed: 3 to 5mm graded, washed, inert quartz gravel.
6’’ sump with end cap
Note: 4 6” production bores will be drilled on the same drilling pad as the most productive exploration holes.