## Slide 1: ANNEX 1. Drawings
Toker Hospital Toilets and Septic Tank
Mohammed Abdalla
TITLE：
DATE： August 2021
Plan View
Legend | Description |  | No.
 | 900x2000 Lockable from outside |  | R1, L1
 | 900x2000 | Lockable from both sides, 400w x200h vent hole with fins | R1, L1
 | 800x2000 |  | R4
 | 800x1000 2 piece, 1 outside open, latch, burglar bar inside, |  | 2
 | 400x300 Ventilation with fixed fins |  | 6
 | Stool bowl, 4in PVC pipe 1400 |  | 2
 | Crouching seat, 4in PVC pipe 1400 |  | 4
Notes:
Walls
1. All walls shall be made of well burned bricks with thickness of 200mm.
2. Lay 3 courses in English Cross . After 4th course of bricks, use brick conforce (force wire).
3. Apply plaster 18mm from floor to ceiling internal, and 15mm for external walls.
Toilet Rooms
1. Finished wall shall be shining.
2. Wastewater shall not come out from the door. Spilled water shall go into either shower drain or sitting hole.
3. Shower nozzles can be small but tamper resistant.
4. Attach a hook inside all D2 and D3 doors.
5. Place a shoe rack and additional hook on the wall in shower rooms.
6. Make threads around 4in PVC pipes and tighten tying wires on upper portion where embedded in the slab.
D1
D2
W1
W2
D3
1500
1500
1500
2000
2000
1500
10000 C/C
3000
2000
2000
7000 C/C
Women Site
Men Site
D3
D2
D2
D3
D3
D3
W2
W2
W2
W2
W2
W2
D1
D1
200

## Slide 2
TITLE：
DATE： August 2021
Front Right
Rear Left
G.L.
Base Beam
Ring Beam
Slab
Toker Hosbital Toilets and Septic Tank
Mohammed Abdalla
Elevation Views

## Slide 3
TITLE：
DATE：
Bottom Slab Plan View
300
300
6 No. 16mmφ Y-Bar
8mmφ Ring, 200mm c/c
1:2:4 Concrete
Section A1-A1
1:3:6 Plain Concrete
1:2:4 Reinforced Concrete
150
50
Conforce 86
Brick-force every 4 courses
Well burned ordinary brick
300
Bonding mortar max. 15mm
Foundation & Wall
10000
6500
3500
2000
2000
4000
Excavation Line
GL－3050
GL－3300
A2
A2
5500
11500
A1
A1
10000
6500
3500
2000
2000
4000
Primary Pit
Secondary Pit
Pit Wall Plan View
B1
B1
Section A2-A2
Drainage to Soak Away
Sitting Hole Pipe
Shower
Hand Wash Basin
G.L.
Working Level
Holes
2600
200
Section B1-B1
1000
5000
Working Level
G.L.
100mm RC slab with Conforce 86 on 50mm PC
4000
300
200x300 RC Beam with 6 No. 16mmφ iron bars. See Beam Plan View
2 coats bitumen on 25mm thick plastering
2 No. 500x500mm Concrete Manholes in 100mm thick slab
1000W x 800H Open partition
2 Holes
Foundation Beam 300x300
Brick Wall 300mm
Notes:
1. Size of excavation (11,500L x 5,500W x 3,000D) allows 600 working space between lining and soil walls for plastering and painting.
2. Make the bottom completely flat. No filling back allowed.
3. Apply blinding 50mm.
4. Draw wall lines and set dual 16φ Y-bars along the lining and partition walls. Lay Conforce 86 and tie with Y-bars each other.
5. 2 holes on the partition wall is 2340mm from slab and the bottom of outlet drainage pipe to soak away is 2600mm from the slab that is the working level in septic tank.
6. Finish the top of lining completely flat.
7. Plaster 25mm in and out of all walls.
8. Paint 2 coats of bitumen in and out of lining.
9. Fill gaps around lining layer by layer and compact it each time until completely filled up to ground level.
Toker Hosbital Toilets and Septic Tank
Mohammed Abdalla
Septic Tank
Coming from internal toilets of the Hospital

## Slide 4
TITLE：
DATE： August 2021
Section A2-A2
200
300
6 No. 16mmφ Y-Bar
8mmφ Ring, 200mm c/c
1:2:4 Concrete
Section A1-A1
150
500
400
Granite Stone
≒ 100mm filled with cement sand
G.L.
200
550
1:2:4 R.C
Notes:
1. Start foundation excavation after refilling the gap around septic tank lining.
2. Bottom of foundation shall be very flat.
3. Fill hardcore pieces carefully, rammer on top, fill half with cement sand, repeat those up to 500 mm.
4. Lay beam with 4 bar and 1:2:4 concrete. The top shall be very flat and at ground level.
5. Top of foundation wall shall be leveled against septic tank lining.
6. Back fill inside foundation walls layer by layer with marram (rough sand), compact and repeat it up to top.
Notes:
1. Ends of iron bars shall be bent 90o and beam intersections shall be tied each other.
2. Forms shall be strong to resist wet concrete pressure.
3. Do not use much water to mix to minimize losing cement juice.
4. Vibrate thoroughly. No babbles allowed in beams.
Base Beam Plan View
Toker Hosbital Toilets and Septic Tank
Mohammed Abdalla
Plan Views of Foundation and Base Beam
8mmφ Ring, 200mm c/c
4 No. 12mmφ Y-Bar

## Slide 5
TITLE：
DATE： August 2021
Hand Washing Basin Side A1-A1
Toilet Room Side A2-A2
200
200
100
200
Center of Door
Vent Hole on Door
A1
A1
A2
A2
Toker Hosbital Toilets and Septic Tank
Mohammed Abdalla
Inside elevation views

## Slide 6
Legend | Description | No.
 | Pump | 1
 | Shower Nozzle 1/2in | 2
 | Tap 1/2in | 12
 | Valve 1/2in 3/4in | 2 7
 | Pipe 1/2in GI (open)/PVC (buried) | 
 | Pipe 3/4in GI (open)/PVC (buried) | 
 | Pipe 1/2in GI (open)/PVC (buried) | 
TITLE：
DATE： August 2021
Water Supply System Diagram
S
V
T
P
Soil
GL
1000
100
100
5000
100
100
700
1550
50
Honeycomb Brick
Brick
Hardcore (150mm gauge)
4” PVC from Septic Tank
RC with 10Φ 150x150
Manhole Lid 450x450
DPM
400
400
2000
Soak-away
Plan View
2000
1000
100
100
From Septic Tank
Soak-away
Chamber
Slab
400
150
400
Manhole Detail
Outlet
Inlets
Brick
Notes:
Water Supply
1. The first valve and the water pump shall be embedded under the terrace in front of overseer shelter’s door. The lid shall be steel so that easy to operate. The pump is operated by the switch on the outlet in the shelter.
Waste Water
1. Shower waste from women site goes into the septic tank straight.
2. Manhole on the merge from hand washing basins shall have sand trap that shall be cleared periodically.
Soak Away
1. Lay ring blinding as thick as 50mm in the bottom of the soak away.
2. Soak away lining is made of bricks. Bottom half shall be honeycomb that have 3 small spaces each course to let waste go out.
3. Outside over the GL shall be plastered.
V
V
V
V
V
V
V
V
P
Manhole Detail
Toker Hosbital Toilets and Septic Tank
Mohammed Abdalla
Water, Drainage, and Soak Away

## Slide 7
TITLE：
DATE：
Legend | Description | No.
 | Utility Power Meter | 1
 | Distribution Box | 1
 | Light (indoor) | 4
 | Light (outdoor, rain proof) | 4
 | Switch | 4
 | Outlet (single) | 1
 | Outlet (double) | 1
 | Water Pump 1/2in | 1
 | Float Switch (water tank) | 1
Notes:
Cables shall be buried in walls or roofs in conduit. The surface shall have no shades.
Set conduits for water pump under and through the slab.
Set conduits as necessary through the top beam.
The inlet tank is equipped with a float switch so that pump stops automatically when it becomes full.
Roof
Wall
200
250
Room Light Installation
M
DB
P
FS
M
DB
Men Site
Women Site
Cabling
P
P
FS
Women Site
Men Site
Toker Hosbital Toilets and Septic Tank
Mohammed Abdalla
Electricity

## Slide 8
TITLE：
DATE：
Notes:
1. Works shall be commenced after the base slab level shall be defined.
2. The GL at each site to be confirmed again to set ±0 at the entrance of slope.
3. The inclination of slopes is 1/10 (6o).
4. The landing level of slopes shall be 43% of the base slab level from GL.
5. Slope walls and curbs to be plastered and painted.
Side View – Women Site
Side View – Men Site
200T brick wall with brick force on 50T blinding under 200D x200W hardcore
200 x200 brick curbs on 70T RC bed with Con-force 86 on compacted marram (rough sand)
G.L.
Women Site
Men Site
Center of Door
1300
4200
1200
600
10000
1400
1400
Slope 1/10
Slope 1/10
Steps
Curb
Curb
2800
600
Curb
1500
4000
2100
900
4200
1200
1300
7900
1200
4000
Toker Hosbital Toilets and Septic Tank
Mohammed Abdalla
Approach Slopes

## Slide 9
TITLE：
DATE： August 2021
400
400
700
700
450
700
3000
450
100
100
100
800
150
150
400
700
400
400
400
400
700
400
1500
400
100
100
100
800
150
150
400
700
400
400
Men Site
Women Site
Plan View
Elevation View
Side View
Notes:
1. Water pipes and drainage pipes including manhole shall be embedded before the slab concreting.
2. Other works shall be commenced after building the outer walls.
From Water Tank
To Manhole
Toker Hospital Toilets and Septic Tank
Mohammed Abdalla
Hand Washing Basins

## Slide 10
3000mm
G. L
140mm
Elevation and Section View
Title: Fence
800 mm
Granite stone 400 mm Width Cement Mortar 1:6
3000mm
Plain concrete1:3:6 100mm Thickness
G. L
400
400mm
200mm Thickness
600mm
Shidyab Health Center - Fence
Harith Mohammed
DATE： September 2021

## Slide 11
A
4600mm
A
3000mm
150mm
Section A-A
15000mm
30000mm
Title : Fence plan View
Notes:
Excavation size For Strip Foundation (600mm width and 500mm Depth).
Top of foundation shall be very flat.
Red Brick must be well burned and in standard dimension.
Brick wall 200mm Thickness , with 1:6 Cement mortar.
Brick Piers 400x400mm must be provided Every Three meters.
Smooth Plastering in and out
Painting with Pomastic at least three
layers
8. The western side of the fence should have 60 cm extra foundation depth
3000mm
Shidyab Health Center - Fence
Harith Mohammed
DATE： September 2021
North

## Slide 12
Angle steel section
70 x70x 5mm thickness
3000 mm
500
G.L
500
Lock
1000 mm
Plain Concrete with slope 1:10 from Center to Edges
Plain concrete 500x500x500mm
400mm
Title : Gate View
H Section steel posts 120X6 mm Thickness
600x600mm Brick Piers
Angle section 50x50x5mm
1800mm
Angle section 50x50x5
NOTES:
1. All Metal part shall be painted with primer coat of rust resistant.
2. PVC wire mish shall be full fixing on frame using pvc coated wire
PVC coated wire mish
Shidyab Health Center – Fence
Harith Mohammed
DATE： September 2021

## Slide 13
Shidyab Health Center Toilet
Abdelkhalik Mahgoub
TITLE：
DATE： September 2021
Plan View
4000 c/c
2000c/c
Base beam plan
A1
300
300
5300
Section A1-A1
150mm thickness slab/ Ꝋ12
150 mm c/c
Bothway
Pit slab reinforcing plan
A
A
pit side view
A1
300
300
6 No. 16mmφ Y-Bar
8mmφ Ring, 150mm c/c
1:2:4 Concrete
Top slab beam section
5600c/c
2000 c/c

## Slide 14
Shidyab Health Center Toilet
Abdelkhalik Mahgoub
TITLE：
DATE： September 2021
Notes:
Walls
1. All walls shall be made of well burned bricks with thickness of 200mm.
2. Lay 3 courses in Soldiering and every 4th course in Headers. After 2nd course of headers, use brick conforce (force wire).
3. Apply plaster 18mm from floor to ceiling internal, and 15mm for external walls.
Toilet Rooms
1. Finished wall shall be shining.
2. Wastewater shall not come out from the door.
3. Attach a hook inside all D3 doors.
4. Make threads around 4in PVC pipes and tighten tying wires on upper portion where embedded in the slab.
3000
5000
Notes:
1. Size of excavation (5000L x 3,000W x 5,,000 D) allows 600 working space between lining and soil walls for plastering and painting.
2. Make the bottom completely flat. No filling back allowed.
3. Apply blinding 50mm.
4. Draw wall lines and set dual 16φ Y-bars along the. Lay Conforce 86 and tie with Y-bars each other.
5. Finish the top of lining completely flat.
6. Plaster 25mm in and out of all walls.
7. Paint 2 coats of bitumen in and out of lining.
8. Fill gaps around lining layer by layer and compact it each time until completely filled up to ground level.
Rear view

## Slide 15
Shidyab Health Center Toilet
Abdelkhalik Mahgoub
TITLE：
DATE： September 2021
Notes:
1. Ends of iron bars shall be bent 90o and beam intersections shall be tied each other.
2. Forms shall be strong to resist wet concrete pressure.
3. Do not use much water to mix to minimize losing cement juice.
4. Vibrate thoroughly. No babbles allowed in beams.
Section A2-A2
150
500
400
Granite Stone
≒ 100mm filled with cement sand
G.L.
200
550
1:2:4 R.C
8mmφ Ring, 200mm c/c
4 No. 12mmφ Y-Bar
Notes:
1. Start foundation excavation after refilling the gap around pit lining.
2. Bottom of foundation shall be very flat.
3. Fill hardcore pieces carefully, rammer on top, fill half with cement sand, repeat those up to 500.
4. Lay beam with 6 bar and 1:2:4 concrete. The top shall be very flat and at ground level.
5. Top of foundation wall shall be leveled against septic tank lining.
6. Back fill inside foundation walls layer by layer with marram (rough sand), compact and repeat it up to top.

## Slide 16
Shidyab Health Center Toilet
Abdelkhalik Mahgoub
TITLE：
DATE： September 2021
D3
W2
W2
D3
2000 C/C
Bathroom plan
1000
D2
4000 C/C
D2
A2
A2
Legend | Description |  | No.
 | 900x2000 | Lockable from both sides, 400w x200h vent hole with fins | 2
 | 800x2000 |  | 2
 | 800x1000 2 piece, 1 outside open, latch, burglar bar inside, |  | 2
 | 400x300 Ventilation with fixed fins |  | 2
 | Stool bowl, 4in PVC pipe 1400 |  | 2
 | Crouching seat, 4in PVC pipe 1400 |  | 2
D2
W1
W2
D3
Notes:
1. Water pipes and drainage pipes including manhole shall be embedded before the slab concreting.
2. Other works shall be commenced after building the outer walls.

## Slide 17
TITLE：
DATE： September 2021
Shidyab Health Center Toilet
Abdelkhalik Mahgoub
Plan Views of Foundation and Base Beam
G.L + 0.00
Ordinary red bricks wall(thick. 20 cm)
Hole bottom Level -5000
Floor Slab Level +600
Ventilation pipe-PVC 4'' Rectangular steel pipe (3*6)
Zinc Corrugated Sheet Rectangular steel pipe (3*6)
Crouching Seat
R.C. Roof Slab (150 mm) @15cm C/C
5000
1.700
900
4000
1000
1000
2.000
300
Truss Roof Top Level + 2.850
Truss Roof Bottom Level + 2.305
3.105
2.600
2.305
Plain Concrete 125 mm
R.C Concrete beam 20*25 cm
Granite Stone Foundation
500 mm*400 mm with sand mortar
400
500
800
400
500
with cement Mortar 1:6
R.C Ring 150mm Thick
P.C Ring 100mm
Thick Natural Soil
400 250150
900
600
5600
1.900
G.L+ 0.00
Precast RC beam 250*200mm 4 No. 12
mm@15cm C/C,
300 mm Ordinary Brick wall
600
River sand 100mm Thick
1200
Granite Stone Foundation 500mm

## Slide 18
TITLE：
DATE： September 2021
Shidyab Health Center Toilet
Abdelkhalik Mahgoub
Side Elevation
2200
.200 250
Ventilation pipe-PVC 4''
Rectangular steel pipe (3*6)
Zinc Corrugated Sheet
900
4100
2900
600
2300
2200
600
2.000

## Slide 19
TITLE：
DATE： September 2021
Shidyab Health Center Toilet
Abdelkhalik Mahgoub
Top View
4600
30000
15000
8200
60
60
3350
1150
1150
4000
1550
2550
2100
3450
2100
غرفة التحصين
مكتب الدكتور
مكتب التغذية
4000 C/C
2000
2000
2000
1200
D3
D3
D2
D2
1200
1200
Ramp
Ramp
stairs

## Slide 20
Angle steel section
50 x50x 5mm thickness
2500 mm
400
Lock
Plain concrete 400x400x400mm
400mm
Title : Gate View
Angle Section steel posts 70X70X7 mm Thickness
1400 mm
Angle section 25x25x3
NOTES:
All Metal parts shall be painted with primer coat of rust resistant.
Telegraib Health Center
Harith Mohammed
DATE： September 2021
Plain concrete 100mm Thickness

## Slide 21
Tube steel section
60 x30x 2mm thickness
1000 mm
Title : Fence View
600 mm
NOTES:
All Metal parts shall be painted with primer coat of rust resistant.
Marafeet Health Center
Harith Mohammed
DATE： September 2021
200 mm
150 mm
Angle steel section
37.5 x 37.5 x 3mm thickness
Barbed Wire

## Slide 22
Angle steel section
50 x50x 5mm thickness
1900 mm
Lock
Title : Gate View
Existing Column
1800 mm
Angle section 25x25x3mm
Marafeet Health Center
Harith Mohammed
DATE： September 2021
2mm thick steel plate